# HydroMonitor library reference.

There are lots of different sensors and other peripherals supported by the library, which can be switched on and off as needed through #define statements.

Supported pin connections:
- direct MCU pin: name_PIN
- PCF8574 port extender connection: name_PCF_PIN
- MCP23008 port extender connection: name_MCP_PIN
- MCP23017 port extender connection: name_MCP17_PIN
- ADS1115 quad ADC connection: name_ADS_PIN

Not all sensors offer the option to connect through a port extender, other sensors don’t need pin definitions as they are read through I2C.

All modules and sensors implement the following functions:
- void begin(HydroMonitorCore::SensorData *sd, HydroMonitorLogging *l, ...) to initialise the module or sensor. Takes at least pointers to the SensorData and Logging objects as parameters, extra parameters include pointers to e.g. a port extender. This depends on the configuration used.
- void settingsHtml(ESP8266WebServer*) sends the module/sensor settings as html formatted table row (<tr>) and two columns to the connected client.
- bool settingsJSON(ESP8266WebServer*) sends the sensor settings as JSON formatted string to the connected client. Returns true if it has any settings, false if empty (needed for proper JSON formatting).
- void updateSettings(ESP8266WebServer*) reads the key/value pairs of a POST form as sent by the client, and updates its settings as appropriate. The modules do their own data validation.

All sensors also implement the following functions:
- void readSensor(bool readNow = false) takes a reading from the sensor once every REFRESH_SENSORS ms, or immediately if readNow = true. The reading is stored in the sensorData object.
- void dataHtml(ESP8266WebServer*) sends the sensor reading as html formatted table row (<tr>...</tr>) and two columns to the connected client.

## Water level sensor
Measures the water level in the reservoir; returns the value in % of maximum fill level. To use a water level sensor: USE_WATERLEVEL_SENSOR and import HydroMonitorWaterLevelSensor.h.
Available sensors:
- HC-SR04 ultrasound sensor: USE_HCSR04
  Pin connections:
  echo: ECHO_PIN (must be a direct connection to the MCU for proper timing).
  trig: TRIG_PIN (_PCF, _MCP, _MCP17 are available).
- MS5837 pressure sensor: USE_MS5837
  Must be used together with an atmospheric pressure sensor. Sensor also measures the water temperature. Connects over I2C.
- MPXV5004/MP3V5004 pressure sensor (differential; pressure tube): USE_MPXV5004
  Pin connections:
  MPXV5004_PIN, MPXV5004_ADS_PIN
- Bubbler control, so it can be switched off during reading: USE_BUBBLER
  Pin connections:
  BUBBLER_PIN (_PCF, _MCP, _MCP17 are available).
- DS1603L ultrasound sensor: USE_DS1603L
  This sensor connects through a serial interface, which is passed to the sensor’s begin() function.
- Float switches: three switches, to detect a low, medium and high water level: USE_FLOATSWITCHES.
  Pin connections:
  FLOATSWITCH_HIGH_PIN (_PCF, _MCP, _MCP17 are available).
  FLOATSWITCH_MEDIUM_PIN (_PCF, _MCP, _MCP17 are available).
  FLOATSWITCH_LOW_PIN (_PCF, _MCP, _MCP17 are available).
  Float switches are expected to be wired between GND and the pin, the module will enable the pin’s pull-up resistor.
## EC sensor
Measures the water conductivity, returns values in mS/cm based on the calibration done. Has a number of calibration functions offering a user interface through the web site. To use an EC sensor: USE_EC_SENSOR and import HydroMonitorECSensor.h.
Available sensors:
- the normal EC sensor, connected to three MCU pins:
  CAPPOS_PIN
  CAPNEG_PIN
  EC_PIN
- the external isolated sensor board (pH, water temperature and EC): USE_ISOLATED_SENSOR_BOARD and import HydroMonitorIsolatedSensorBoard.h. Data is transmitted through a serial pin.
  Pin connection (Rx only, as we only receive data):
  ISOLATED_SENSOR_BOARD_RX_PIN2
## Water temperature sensor
Measures the water temperature in °C. To use a water temperature sensor: USE_WATERTEMPERATURE_SENSOR and import HydroMonitorWaterTempSensor.h.
Available sensors:
- NTC probe: USE_NTC
  Pin connection:
  NTC_PIN, NTC_ADS_PIN
  Extra parameters:
  nominal resistance of the NTC in Ohm: THERMISTORNOMINAL <resistance>
  nominal temperature of the NTC in °C: TEMPERATURENOMINAL <temp>
  B-coefficient of the NTC: BCOEFFICIENT <value>
  Series resistor value in Ohm: NTCSERIESRESISTOR <resistance>
  Maximum reading of the ADC (Vin = Vcc): ADCMAX <value>
- DS18B20 probe: USE_DS18B20
  Use of this sensor requires a pointer to a OneWire object to be passed on to the begin() function of HydroMonitorWaterTempSensor.
  Pin connection:
  ONE_WIRE_BUS
- MS5837 pressure sensor: see “water level sensor”.
## Atmospheric temperature, humidity and pressure.
The main atmospheric conditions, enabled depending on which are of interest and the connected sensor(s).
Temperature: USE_TEMPERATURE_SENSOR and import HydroMonitorTemperatureSensor.h.
Humidity: USE_HUMIDITY_SENSOR and import HydroMonitorHumiditySensor.h.
Pressure: USE_PRESSURE_SENSOR and import HydroMonitorPressureSensor.h.
Available sensors:
- DHT22 humidity and temperature sensor. The DHT22 has to be initialised first, then a pointer to this object is passed on to the humidity and temperature objects.
  Pin connection:
  DHT22_PIN (must be a direct MCU connection).
- BMP180 and BMP280 pressure and temperature sensor. The BMP180/280 has to be initialised first, then a pointer to this object is passed on to the pressure and temperature objects.
- USE_BME280 pressure, temperature and humidity sensor. The BMP180/280 has to be initialised first, then a pointer to this object is passed on to the pressure and temperature objects.
## pH sensor
Measures the pH of the water. To use a pH sensor: USE_PH_SENSOR and import HydroMonitorpHSensor.h.
Available sensors:
- Sensor connected directly to an analog input.
  Pin connection:
  PH_SENSOR_PIN, PH_SENSOR_ADS_PIN
- Isolated sensor board: see EC Sensor.

## DO sensor, ORP sensor
Not implemented yet.
To enable USE_DO_SENSOR and USE_ORP_SENSOR.
Pin connections: DO_SENSOR_PIN / DO_SENSOR_ADS_PIN, ORP_SENSOR_PIN / ORP_SENSOR_ADS_PIN
## Brightness sensor
Measure the brightness of the sunlight. To use a brightness sensor: USE_BRIGHTNESS_SENSOR and import HydroMonitorBrightnessSensor.
Available sensors:
- TSL2561 lux sensor: USE_TSL2561
- TSL2591 lux sensor: USE_TSL2591
## UV sensor
Not implemented.

## WiFi LED
Use an LED to indicated the WiFi status.
On: WiFi connected.
Blinking, 1 Hz: WiFi not connected.
Blinking, 3 Hz: in OTA recovery window.
Blinking, 5 Hz: OTA update in progress.
To use a WiFi LED: USE_WIFILED (no extra modules to be imported)
Pin connections: WIFILED_PIN (_PCF, _MCP, _MCP17 are available).
## Growlight
Switches on based on time or automatic based on the reading of the brightness sensor. To use the growlight: USE_GROWLIGHT and import HydroMonitorGrowlight.h.
Implements functions:
- checkGrowlight(): to be called frequently, handles the growlight automatic switching.
- on(): switches the growlight on, disables automatic handling.
- off(): switches the growlight off, disables automatic handling.
- automatic(): returns control to automatic handling.
Pin connection: GROWLIGHT_PIN (_PCF, _MCP, _MCP17 are available).
## Fertiliser
Add fertiliser based on the current EC reading, through two peristaltic pumps. Requires an EC sensor to be connected. To use the fertiliser pumps: USE_FERTILISER and import HydroMonitorFertiliser.h.
Implements functions:
- doFertiliser(): to be called frequently, handles the automatic fertiliser adding.
- measurePumpA(), measurePumpB(): run this pump for exactly 1 minute to measure the flow.
Pin connections:
FERTILISER_A_PIN (_PCF, _MCP, _MCP17 are available).
FERTILISER_B_PIN (_PCF, _MCP, _MCP17 are available).
## pH adjuster
Lowers the pH based on the current pH reading, through a peristaltic pump. Requires a pH sensor to be connected. To use the pH-minus pump: USE_PHMINUS and import HydroMonitorpHMinus.h.
Implements functions:
- dopH(): to be called frequently, handles the automatic pH-minus adding.
- measurePump(): run this pump for exactly 1 minute to measure the flow.
Pin connections:
PHMINUS_PIN (_PCF, _MCP, _MCP17 are available).
# Reservoir level management
Automatically adds water to the reservoir when it drops below a certain level. To use the reservoir level management: USE_RESERVOIR and import HydroMonitorReservoir.h.
Implements function:
doReservoir(): to be called frequently, handles the water level and switching on/off the water inlet.
Pin connections:
- WATER_INLET_PIN (_PCF, _MCP, _MCP17 are available): the pin that switches on/off the water inlet solenoid.
- LEVEL_LIMIT_PIN (_PCF, _MCP, _MCP17 are available): a limit switch, to raise an alarm when the reservoir is critically full. If not defined, it’s ignored.
- LEVEL_ALARM_PIN (_PCF, _MCP, _MCP17 are available): (not implemented) output connected to an active buzzer, to create an audible alarm.
## Ventilation fan (not implemented)
To run a ventilation fan based on air temperature or time. To use: USE_VENTILATION and import HydroMonitorVentilation.h.
Implements function:
doVentilation(): to be called frequently, handles the switching on/off the ventilation system.
Pin connections:
VENTILATOR_PIN (_PCF, _MCP, _MCP17 are available): the pin that switches on/off the ventilation fan.
## Drainage pump
To completely drain the reservoir, used for fertiliser solution maintenance and for draining the reservoir if the water level has become too high. To use: USE_DRAINAGE_PUMP and import HydroMonitorDrainage.h.
Implements function:
doDrainage(): to be called frequently, handles the reservoir drainage.
Pin connections:
DRAINAGE_PIN (_PCF, _MCP, _MCP17 are available): the pin that switches on/off the drainage pump.
## LCD display (not implemented)
## To produce output to a 2004 LCD display, showing the current status of the system. To use: USE_2004LCD and import HydroMonitorLCDDisplay.h.
Implements function:
## doDisplay(): to be called frequently, handles the display updates.
## Peripherals
- USE_I2C starts the I2C bus (redundant?).
- USE_MICROSD log to MicroSD card instead of internal SPIFFS (not implemented).
- USE_FACTORY_RESET use the Program button as factory reset: press 5 seconds for a complete clearing of the logs and stored settings.
- USE_PCF8574 use the PCF8574 8-bit port extender.
- USE_ADS1115 use the ADS1115 quad external ADC.
- USE_MCP23008 use the MCP23008 8-bit port extender.
- USE_MCP23017 use the MCP23017 16-bit port exetnder.
- USE_SERIAL send log messages to the Serial console.
- USE_24LC256_EEPROM use an external 24LC256 I2C EEPROM IC instead of the internal Flash to store settings and current system status.
- USE_OTA enables OTA software updates.
## Default settings
- LOGGING_USERNAME, LOGGING_PASSWORD: the username and password for logging to the external MySQL database.
- LOG_SERIAL send log messages to the Serial console (requires USE_SERIAL)
- LOG_MYSQL send log messages and sensor data to an external MySQL database.
- LOGLEVEL sets the current loglevel. Valid levels are: LOG_TRACE / LOG_INFO / LOG_WARNING / LOG_ERROR / LOG_OFF
- OTA_PASSWORD the password of this system for OTA software updates.